Annexure F

Access LAN, WiFi – APs and Core Switches Technical Specifications

| ID | Specifications | Compliance | Yes | No |
| --- | --- | --- | --- | --- |
| 1 | Broad Features |  |  |  |
| a | The Switch must have dual Power Supply -For high availability |  |  |  |
| b | The Switch must have 24P PoE+ |  |  |  |
| c | The Switch must have 48P PoE+ |  |  |  |
| d | The Switch must be stackable capabilities |  |  |  |
| e | The Switch will support 4 x 10 GE 2 x 40 GE or 4x Multigigabit Network Module(Nbase-T) |  |  |  |
| f | The Switch must be Cloud ready |  |  |  |
| 2 | Performance |  |  |  |
| a | Minimum 205Gbps switching capacity and 150 Mpps forward rate |  |  |  |
| B | Up to 32 000 MAC address, equal count of unicast address and 64 000 of flexible NetFlow entries |  |  |  |
| C | Switch must support stacking bandwidth minimum of 475Gbps |  |  |  |
| D | Switch must have Mean Time failure of 300 000 hours |  |  |  |
| 3 | Network Operating System |  |  |  |
| a | The platform shall have an open standard, modular, extensible operating system that shall support a wide range of automation features and provides robust open APIs over NETCONF using YANG data models |  |  |  |
| b | The operating system shall support resilience through Seamless software upgrades and patching |  |  |  |
| c | The software shall support patching, which provides fixes for critical bugs and security vulnerabilities without having to wait for the next maintenance release |  |  |  |
| d | The switch shall support Streaming telemetry, sampled NetFlow, Switched Port Analyzer, Remote SPAN. |  |  |  |
| 4 | Power |  |  |  |
| a | Shall have at least 3 fans and in case of failure of any one of those the other fans should automatically speed up. Fans should be field replaceable |  |  |  |
| b | Shall carry power savings mechanism wherein it should reduce the power consumption on ports not being used |  |  |  |
| 5 | Application Visibility |  |  |  |
| a | The Switch should support Flexible NetFlow on all ports of the switch for Ingress and Egress Traffic |  |  |  |
| B | The Switch should support at least 64000 Flows per switch |  |  |  |
| C | The Switches when stacked together should be capable to exporting the flow independently / directly to the FnF Collector |  |  |  |
| 6 | Layer – 2 Features |  |  |  |
| a | IEEE 802.1Q VLAN encapsulation. Up to 4000 VLANs per switch or stack and Up to 4000 VLAN IDs |  |  |  |
| b | Spanning-tree Port Fast and Port Fast guard for fast convergence |  |  |  |
| c | 802.1d, 802.1s, 802.1w, 802.3ad etc |  |  |  |
| d | IGMP snooping v1, v2 and v3 |  |  |  |
| e | Port Aggregation Protocol (PAgP), Link Aggregation Protocol (LACP) |  |  |  |
| 7 | Layer - 3 Features |  |  |  |
| a | Basic IP unicast routing protocols (static, RIPv1, and RIPv2) |  |  |  |
| B | Spanning Tree Protocol , Rapid STP , VLAN Trunking Protocol , trunking, Private VLAN , dynamic voice VLAN, IPv6, PnP, 802.1Q tunneling, Routed Access – OSPF and RIP, Policy-Based Routing , Virtual Router Redundancy Protocol , Internet Group Management Protocol, PIM Stub, Weighted Random Early Detection , First Hop Security , 802.1X, MACsec-128, Control Plane Policing , SGT Exchange Protocol , IP SLA Responder, SSO, EIGRP Stub, Microflow Policing, Class-Based Weighted Fair Queuing , hierarchical QoS , Application Reporting, Syslog, SNMP |  |  |  |
| 8 | Convergence and QoS |  |  |  |
| a | The Switch should support Advanced Modular Wired and Wireless QoS Policies The Switch should be capable of Queuing, Policing, Shaping, and marking Wired and Wireless Traffic based on Class of Service (CoS) or DSCP. |  |  |  |
| b | The Switch should be capable of Queuing, Policing, Shaping, and marking Wired and Wireless Traffic based on Class of Service (CoS) or DSCP. |  |  |  |
| c | Granular Rate Limiting function to guarantee bandwidth in increments as low as 8 kbps. |  |  |  |
| d | Up to 64 aggregate or individual policers for per Fast Ethernet or Gigabit Ethernet port. |  |  |  |
| e | Should support per-port Rate Limiting setting ingress enforced maximums. |  |  |  |
| f | Should support LLDP-MED (Media Endpoint Discovery). |  |  |  |
| g | The switch should support 8 queues per port and strict priority queue which helps ensure that the highest-priority packets are serviced ahead of all other traffic. |  |  |  |
|  | Should support IEEE 802.1AB Link Layer Discovery Protocol (LLDP). |  |  |  |
|  | Should support IP multicast Snooping (data-driven IGMP). |  |  |  |
| 8 | Security |  |  |  |
| a | Should support Port security. |  |  |  |
| b | Should support Access control lists (ACLs) to provide IP Layer 3 filtering based on source/destination IP address/subnet and source/destination TCP/UDP port number. |  |  |  |
| c | Should support IEEE 802.1X user authentication, Web-based authentication, and MAC-based authentication. |  |  |  |
| d | Should support DHCP Snooping. |  |  |  |
| e | Should support TACACS+ and RADIUS authentication for secure switch CLI logon. Should support SSHv2 and SSL allowing secure access to the switch |  |  |  |
| 9 | Network Security features |  |  |  |
| a | IEEE 802.1x to allow dynamic, port-based security, providing user authentication |  |  |  |
| b | Unicast MAC filtering to prevent the forwarding of any type of packet with a matching MAC address |  |  |  |
| c | Unknown unicast and multicast port blocking to allow tight control by filtering packets that the switch has not already learned how to forward. |  |  |  |
| d | Support for up to One thousand access control entries (ACEs). |  |  |  |
| 8 | Resiliency and High availability |  |  |  |
| a | Should support IEEE 802.3ad Link Aggregation Control Protocol (LACP). |  |  |  |
| b | Should support IEEE 802.1s Multiple Spanning Tree Protocol. |  |  |  |
| c | Should support external redundant power supply. |  |  |  |
| 9 | Advanced Features |  |  |  |
| a | The switch should have feature to provide real-time network event detection and onboard automation. |  |  |  |
| b | The switch should support Multicast VLAN Registration. |  |  |  |
| C | The Switch should support IEEE 802.1AE MACsec. MACsec should provide Layer 2, line rate Ethernet data confidentiality and integrity on host facing ports, protecting against man-in-the-middle attacks (snooping, tampering, and replay). |  |  |  |
| d | The switch should support Enhanced Energy management feature along with various policy support. The switch should have support capabilities to support energy consumption, energy reports and energy management |  |  |  |
| e | The switch should support feature allowing unidirectional links caused by incorrect fiber-optic wiring or port faults to be detected and disabled on fiber-optic interfaces. |  |  |  |
| f | The switch should have feature to provide automatic configuration as devices connect to the switch port, allowing auto detection and plug and play of the device onto the network. |  |  |  |
| 10 | Management |  |  |  |
| a | The switch shall support Bluetooth dongle to enable wireless interface as an IP management port interface for configuration and troubleshooting. Switch must be cloud management ready |  |  |  |
| b | Layer 2 traceroute to ease troubleshooting by identifying the physical path that a packet takes from source to destination. Email alerts for switch management tools |  |  |  |
| c | Trivial File Transfer Protocol (TFTP) to reduce the cost of administering software upgrades by downloading from a centralized location. Ports management from GUI based dashboard |  |  |  |
| d | Network Timing Protocol (NTP) to provide an accurate and consistent timestamp to all intranet switches. Zero touch provisioning is essential |  |  |  |
| e | RMON I and II standards Per port and per client usage statistics |  |  |  |
| f | SNMPv1, SNMPv2c, and SNMPv3 Secure user schedules |  |  |  |
| g | The switches must be IoT ready |  |  |  |

Annexure F- WLAN – WiFi Technical Specification

| 11 | WLAN Technical Specification | Compliance | Yes | No |
| --- | --- | --- | --- | --- |
| A | Controller’s Traits Must be Cloud ready Must Connect up to 3000 APs in one instance Maximum Clients must connect to 10, 000 clients Thoroughput 5Gbps to 10Gbps symmetrical Uplinks 2*10Gbps – Multigigabit Fibre preferable VLANs over 4000 WLANs over 4000 Automated device provisioning Seamless software upgrades and Patching API – Driven configurations Granular visibility Secure boot Encrypted Traffic Analytics Imagine Signing Secure boot Flexible NetFlow Must provide superior Quality of service – QoS Must have strong Guest Management capabilities Must have bandwidth management capabilities Encrypted Traffic Analytics and SD-Access. |  |  |  |
| 12 | Access Points – APs Compulsory Specification |  |  |  |
| a | OFMDA |  |  |  |
| b | MU-MIMO |  |  |  |
| c | Multigigabit support |  |  |  |
| d | Internal Antennae for inside the office |  |  |  |
| e | External Antennae for hallways and open spaces |  |  |  |
| f | Must be ready for IoT |  |  |  |
| g | BLE – 802.15.4 Protocols |  |  |  |
| h | WiFi 6 Certified |  |  |  |
| i | Support 802.11ax for 2.4GHz |  |  |  |
| j | Support 802.11ax for 5GHz |  |  |  |
| k | RF ASIC |  |  |  |
| I | RF Fingerprinting |  |  |  |
| m | Radio 5GHZ 8x8 or dual 2.4 4x4 |  |  |  |
| n | WLAN must be poised to deliver enterprise-grade VoWLAN |  |  |  |
| o | WLAN must be poised to deliver enterprise-grade VideoWLAN |  |  |  |
| p | The ability to detect Rogue APs and disables them |  |  |  |
| q | The APs must have WIPS and WIDS capabilities |  |  |  |
| r | The APs must have Spectrum Intellegence |  |  |  |
| s | The APs Must have location analytics capabilities |  |  |  |
| t | APs must have Fastlocate tech to improve location-refresh rate |  |  |  |

Annexure F- Hubs - Core Switches Specifications

- UK - London

| Switch Model | Ports Requirements | Description | Quantity |
| --- | --- | --- | --- |
| Gigabit Ethernet - Core GbE No PoE | 24 | GbE – Gigabit Ethernet | 2 |
|  | 4 x 10Gb SFP+ Uplinks | Network Modules | 2 |
|  | Software License | IP Services | 2 |
|  | SFP+ | 40Gbps | 4 |
| Gigabit Ethernet - Core SFP+ No PoE | 24 | SFP+ | 2 |
|  | 40Gbps x 4 Uplinks | Network Modules | 2 |
|  | Software License | IP Services | 2 |
|  | SFP+ | SFP+ Gbps - Core | 24 |
|  | SFP+ | Access Switches | 38 |

- USA - Washington DC Core Switches

| Broad Requirement | Ports Requirement | Description | Quantity |
| --- | --- | --- | --- |
| Gigabit Ethernet - Core Gbps No PoE | 24 | GE – Gigabit Ethernet | 2 |
|  | 4 x 40Gb SFP+ Uplinks | Network Module | 2 |
|  | Software License | IP Services | 2 |
|  | SFP+ | 40Gbps | 16 |
| Gigabit Ethernet - Core SFP+ No PoE | 12 | SFP+ | 2 |
|  | 40Gbps SFP+ Uplinks | Network Modules | 2 |
|  | Software License | IP Services | 2 |
|  | SFP+ | 10Gbps ¦ 40Gbps – Uplinks | 24 |
|  | SFP+ | Access Switches | 18 |

Annexure F

LAN Switches Ports Density Allocations

| Mission Name | City | Users | C. Switch | LAN Switches | Qty | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| Region - Africa |  |  |  |
| Ivory Cost | Abidjan | 31 | 0 | 48P PoE+ | 1 |  |
| Nigeria | Abuja | 6 | 0 | 12P PoE+ | 1 |  |
| Ethiopia | Addis Ababa | 35 | 0 | 24P PoE Core Switch 6 x 10Gpbs SFPs | 3 1 1 |  |
| Algeria | Algiers | 19 | 0 | 24P PoE+ | 1 |  |
| Jordan | Amman | 19 | 0 | 24P PoE+ | 1 |  |
| Turkey | Ankara | 18 | 0 | 24P PoE+ | 1 |  |
| Madagascar | Antananarivo | 14 | 0 | 24P PoE+ | 1 |  |
| Eritrea | Asmara | 11 | 0 | 24P PoE+ | 1 |  |
| Kazakhstan | Astana | 12 | 0 | 24P PoE+ | 1 |  |
| Mali | Bamako | 16 | 0 | 24P PoE+ | 1 |  |
| Guinea Bissau | Bissau | 5 | 0 | 24P PoE+ | 1 |  |
| Congo | Brazzaville | 13 | 0 | 24P PoE+ | 1 |  |
| Romania | Bucharest | 13 |  | 24P PoE+ | 1 |  |
| Burundi | Bujumbura | 21 | 0 | 24P PoE+ | 1 |  |
| CAR | Bangui | 10 | 0 | 16P PoE+ | 1 |  |
| Egypt | Cairo | 18 | 0 | 24P PoE+ | 1 |  |
| South Africa | Cape Town Airport | 5 | 0 | 16P PoE+ | 1 |  |
| South Africa | Cape Town Parliament | 22 | 0 | 24P PoE+ | 1 |  |
| Benin | Cotonou |  | 0 | 24P PoE+ | 1 |  |
| Guinea | Conakry | 12 | 0 | 24P PoE+ | 1 |  |
| Senegal | Dakar | 18 | 0 | 24P PoE+ | 1 |  |
| Syria | Damascus |  | 0 | 24P PoE+ | 1 |  |
| Tanzania | Daar Es Salaam | 13 | 0 |  |  |  |
| South Africa | Diplomatic Guest House |  | 0 | 24P PoE+ | 1 |  |
| Botswana | Gaborone | 27 | 0 | 36P PoE+ | 1 |  |
| Zimbabwe | Harare | 16 | 0 | 24P PoE+ | 1 |  |
| Indonesia | Jakarta |  | 0 | 24P PoE+ | 1 |  |
| Saudi Arabia | Jeddah | 12 | 0 | 24P PoE+ | 1 |  |
| Southern Sudan | Juba | 9 | 0 | 16P PoE+ | 1 |  |
| Uganda | Kampala | 16 | 0 | 24P PoE+ | 1 |  |
| Sudan | Khartoum | 19 |  | 24P PoE+ | 1 |  |
| Ukraine | Kiev | 10 | 0 | 24P PoE+ | 1 |  |
| Rwanda | Kigali | 14 | 0 | 24P PoE+ | 1 |  |
| South Africa | King Shaka International Airport | 5 | 0 | 16P PoE+ | 1 |  |
| DRC | Kinshasa | 14 |  | 24P PoE+ | 4 |  |
| Nigeria | Lagos | 11 | 0 | 48P PoE+ | 1 |  |
| Gabon | Libreville | 17 | 0 | 24P PoE+ | 1 |  |
| Malawi | Lilongwe | 11 | 0 | 16P PoE | 1 |  |
| Angola | Luanda | 17 | 0 | 24P PoE+ 8P SFP | 4 1 |  |
| DRC | Lubumbashi | 13 | 0 | 24P PoE+ | 1 |  |
| Zambia | Lusaka | 18 | 0 | 48P PoE+ | 1 |  |
| Equatorial Guinea | Malabo | 12 | 0 | 24P PoE+ | 1 |  |
| Mozambique | Maputo | 18 | 0 | 48P PoE+ | 1 |  |
| Lesotho | Maseru | 17 | 0 | 48P PoE+ | 1 |  |
| Swaziland | Mbabane | 13 | 0 | 48P PoE+ | 1 |  |
| Kenya | Nairobi | 29 |  | 48P PoE+ | 1 |  |
| Chad | N’Djamena | 10 | 0 | 24P PoE+ | 1 |  |
| Mauritania | Nouakchott | 7 | 0 | 24P PoE+ | 1 |  |
| Niger | Niamey | 5 | 0 | 24P PoE+ | 1 |  |
| Burkina Faso | Ouagadougou | 5 | 0 | 24P PoE+ | 1 |  |
| Liberia | Monrovia | 5 | 0 | 24P PoE+ | 1 |  |
| Sao Tome & Principe | Sao Tome | 5 | 0 | 24P PoE+ | 1 |  |
| South Africa | Presidential Guest House | 8 | 0 | 16P PoE+ | 1 |  |
| Region -Brasilia | City |  |  |
| Argentina | Buenos Aries | 25 | 0 | 24P PoE+ | 1 |  |
| Venezuela | Caracas | 16 | 0 | 24P PoE+ | 1 |  |
| Peru | Lima | 14 | 0 | 24P PoE+ | 1 |  |
| Mexico | Mexico City | 16 | 0 | 24P PoE+ | 1 |  |
| Chile | Santiago | 23 | 0 | 24P PoE+ | 1 |  |
| Brasilia | Sao Paulo | 22 | 0 | 24P PoE+ | 1 |  |
| Region-London | City |  |  |  |  |  |
| Ghana | Accra | 19 | 0 | 24P PoE+ | 1 |  |
| Switzerland | Bern | 26 | 0 | 48P PoE+ | 1 |  |
| Belgium | Brussels | 52 | 0 | 48P PoE+ | 1 |  |
| Ireland | Dublin | 52 | 0 | 48P PoE+ 16P PoE+ | 2 |  |
| Switzerland | Geneva | 39 | 0 | 48P PoE+ | 1 |  |
| Cuba | Havana | 20 | 0 | 24P PoE+ | 1 |  |
| Jamaica | Kingston | 17 | 0 | 48P PoE+ | 1 |  |
| Portugal | Lisbon | 20 | 0 | 24P PoE+ | 1 |  |
| Spain | Madrid | 23 | 0 | 24P PoE+ | 1 |  |
| Comoros | Maroni | 9 | 0 | 16P PoE+ | 1 |  |
| France | Paris | 49 | 0 | 48P PoE+ | 1 |  |
| Saudi Arabia | Riyadh | 14 | 0 | 24P PoE+ | 1 |  |
| Netherland | The Hague | 27 | 0 | 48P PoE+ | 1 |  |
| England | Whitehall | 22 | 0 | 24P PoE+ | 1 |  |
| The Vatican | Holly See |  | 0 | 16P PoE+ | 1 |  |
| Region- Singapore | City | Users | Core Switch |  |  |  |
| Thailand | Bangkok | 23 | 0 | 24P PoE+ | 1 |  |
| China | Beijing | 51 | 0 | 48P PoE+ | 1 |  |
| Australia | Canberra | 23 | 0 | 24P PoE+ | 1 |  |
| Sri Lanka | Colombo | 13 | 0 | 16P PoE+ | 1 |  |
| Vietnam | Hanoi | 18 | 0 | 24P PoE+ | 1 |  |
| Japan | Hong Kong | 14 | 0 | 24P PoE+ | 1 |  |
| Malaysia | Kuala Lampur | 20 | 0 | 24P PoE+ | 1 |  |
| Philippines | Manila | 12 | 0 | 24P PoE+ | 1 |  |
| South Korea | Seoul | 16 | 0 | 24P PoE+ | 1 |  |
| China | Shanghai | 20 | 0 | 24P PoE+ | 1 |  |
| Fiji | Suva | 8 | 0 | 24P PoE+ | 1 |  |
| Taiwan | Taipei | 17 | 0 | 24P PoE+ | 1 |  |
| Japan | Tokyo | 35 | 0 | 48P PoE+ | 1 |  |
| New Zealand | Wellington | 15 | 0 | 24P PoE+ | 1 |  |
| India | New Dehli | 42 | 0 | 48P PoE+ | 1 |  |
| India | Mumbai | 24 | 0 | 36P PoE+ | 1 |  |
| Jakarta | Philippines | 21 | 0 | 24P PoE+ | 1 |  |
| Singapore | Singapore | 13 | 0 | 24P PoE+ | 1 |  |
| Region- Vienna | City | Users |  |  |  |  |
| Greece | Athens | 15 | 0 | 24P PoE+ | 1 |  |
| United Arab Emirates | Abu Dhabi | 11 | 0 | 24P PoE+ | 1 |  |
| Germany | Berlin | 42 | 0 | 48P PoE+ | 1 |  |
| Hungary | Budapest | 16 | 0 | 24P PoE+ | 1 |  |
| Denmark | Copenhagen | 17 | 0 | 24P PoE+ | 1 |  |
| Qatar | Doha | 9 | 0 | 16P PoE+ | 1 |  |
| UAE | Dubai | 16 | 0 | 24P PoE+ | 1 |  |
| Finland | Helsinki | 13 | 0 | 24P PoE+ | 1 |  |
| Pakistan | Islamabad | 24 | 0 | 36P PoE+ | 1 |  |
| Kuwait | Kuwait City | 13 | 0 | 24P PoE+ | 1 |  |
| Italy | Milan | 13 | 0 | 24P PoE+ | 1 |  |
| Russia | Moscow | 41 | 0 | 48P PoE+ | 1 |  |
| India | Mumbai | 24 | 0 | 36P PoE+ | 1 |  |
| Germany | Munich | 17 | 0 | 24P PoE+ | 1 |  |
| Oman | Muscat | 10 | 0 | 24P PoE+ | 1 |  |
| India | New Delhi | 42 | 0 | 48P PoE+ | 1 |  |
| Norway | Oslo | 12 | 0 | 24P PoE+ | 1 |  |
| Czech Republic | Prague | 14 | 0 | 24P PoE+ | 1 |  |
| Italy | Rome | 27 | 0 | 36P PoE+ | 1 |  |
| Bulgaria | Sofia | 10 | 0 | 24P PoE+ | 1 |  |
| Sweden | Stockholm | 18 | 0 | 24P PoE+ | 1 |  |
| Iran | Teheran | 18 | 0 | 24P PoE+ | 1 |  |
| Poland | Warsaw | 16 | 0 | 24P PoE+ | 1 |  |
| Region- Washington | City | Users | C. Switch | LAN Switches |  |  |
| USA | Washington DC | 62 | 2 GbE SFP | 48P PoE+ 24GbE 24SFP | 2 1 1 |  |
| USA | Chicago | 20 | 0 | 24P PoE+ | 1 |  |
| USA | New York | 64 | 0 | 48P PoE+ 24P PoE+ | 1 1 |  |
| USA | Los Angeles | 16 | 0 | 24P PoE+ | 1 |  |
| Canada | Toronto | 12 | 0 | 24P PoE+ | 1 |  |
| Canada | Ottawa | 23 | 0 | 36P PoE+ | 1 |  |

Annexure F

Monitoring Tools Technical Speciation’s Requirement

| 1 | Network Monitoring Tools Functionality | Compliance | Yes | No |
| --- | --- | --- | --- | --- |
| a | The monitoring application must automatically discover network devices connected to Dirco network – up to 4000 Ports. |  |  |  |
| b | The Application must have NetPath feature to permit trace packet transfers hop-by-hop |  |  |  |
| c | The Monitoring tools must have the following key features: SNMP monitoring Automatically discovers connected network devices Network traffic packet analysis Intelligent network maps with NetPath Create Wi-Fi heat maps |  |  |  |
| d | The monitoring application must have cloud-based SaaS infrastructure monitoring services and with on premise aptitudes. |  |  |  |
| e | AI-based machine learning that provides capacity predictions |  |  |  |
| f | Powerful reporting, analytics, and alerts |  |  |  |
| g | Real-time network device monitoring |  |  |  |
|  | Real – time applications monitoring |  |  |  |
|  | Jitter monitoring – pinpoint area of concern and remediate |  |  |  |
| h | Real-Time NetFlow Traffic Analyzer with ability to produce topology map per subnet segment. |  |  |  |
| i | Automatic Wi-Fi heat maps to augment conspicuousness, control to ensure optimal wireless coverage and general management. |  |  |  |
| j | Monitors bandwidth use per LAN, WAN up to application level. |  |  |  |
| k | Bandwidths allocations and adjustment per subnet |  |  |  |
| l | Reports Alerts Mode: Email SMS Mobile App |  |  |  |
| m | The monitoring tools must be Scalable, cloud-based service suitable for vast network sizes across dispersed geographic locations and topologies. |  |  |  |
| n | The SNMP-based monitoring must have autodiscovery feature |  |  |  |
| o | Other dominant features: Bandwidths Monitoring Sensors Hardware / Cloud Parameters Sensors Network Data usage Meters VoIP Sensors QoS Sensors |  |  |  |
|  | On Premise Server and Cloud performance Monitoring |  |  |  |
|  | Centralized Performance dashboard publication – or GUI |  |  |  |